## Slide 1
DAG2000 Series VoIP Access Gateway
Overview
DAG2000 series voice gateway is a VoIP access gateway based on IP. It is able to provide quality voice service for carrier, enterprise, Village users and company. Supported standard SIP protocol and compatible mainstream IPPBX and softswitch platform.
The Gateway to VoIP World
DAG2000-16S
DAG2000-32S
Product pictures
Key benefits
Primary and secondary SIP account
Flexible set port group
IP trunk
Flexible routing and manipulation
Data/ Voice/ Management VLAN
Voice /FAX/Modem
Traffic Shaping
Firmware update automatically /configure update

## Slide 2
The Gateway to VoIP World
SIP V2.0 (RFC 3261,3262,3264)
SDP (RFC 2327)
REFER (RFC 3515)
RTP/RTCP (RFC 1889,1890)
STUN (RFC 3489)
ARP/RARP (RFC 826/903)
SNTP (RFC 2030)
DHCP/PPPoE
TFTP/HTTP/HTTPS
DNS/DNS SRV (RFC 1706/RFC 2782)
VLAN 802.1P/802.1Q
Voice & FAX
Protocol
Supplement Service
Private Service
Physical Interfaces
Phone ports: 16/24/32FXS, RJ-11
Ethernet Interfaces:
16FXS: 4*RJ-45 10/100Mbps, RJ-45
24FXS: 4* RJ-45 10/100Mbps, RJ-45
32FXS: 4* RJ-45 10/100Mbps, RJ-45
G.711A/U law, G.723.1, G.729A/B
Comfort Noise Generation(CNG)
Voice Activity Detection(VAD)
Echo Cancellation(G.168)
Adaptive (Dynamic) Jitter Buffer
Hook flash test
Programmable Gain Control
T.38/Pass-through/Modem FAX mode,
Up to 14.4kbps
DTMF mode: Signal/RFC2833/INBAND
Inquire LAN port IP *158#
Inquire WAN port IP *159#
Get IP address *150*
Restart*111#
Factory reset*166*000000#
Call waiting
Call transfer(Blind transfer, Attend Transfer , Half blind transfer)
Quick pick
Call forwarding
Hotline
Call hold
DND
3-way conference（1/2/4FXS Support）
Voice mail
Direct IP address call
Decade focused
Creates the high-quality goods

## Slide 3
The Gateway to VoIP World
Network Feature
Power input:100-240VAC,50-60Hz
Power consumption: 24FXS:80W;
32FXS:100W
temperature(operator): 0 ℃ ~ 45 ℃
(storage): -20 ℃ ~80 ℃
Humidity: 10%-90% no condensation
Environment
Call & Route
16FXS:442(L)*280(W)*44(H)mm 3.0kg
24FXS:442(L)*250(W)*44(H)mm 3.5kg
32FXS:442(L)*250(W)*44(H)mm 3.5kg
Dimension & Weight:
CE, FCC
Port group
IP trunk
Primary and secondary SIP account
32 inbound routing
32 outbound routing
Number manipulation
Dial plan set
Maintain & Upgrade
Web based configuration
Telnet configuration
Data backup/restore
Support English and Chinese language
Firmware upgrade by TFTP
Syslog and CDR
Web & telnet login password modify
Factory reset
Automatic time synchronization
SNMP
IVR local maintenance management
NAT (Rout and Bridge)
Static IP, PPPoE, DHCP
DHCP server
IP,TCP, UDP,TFTP, FTP, TCP,ARP,RARP, Ping, NTP, SNTP, Http, DNS, Trancert
Static/dynamic ARP
Authentication
Gateway
Power adapter
RJ-45 Network cable
User’s Manual CD
Packing Content
Customer first
Services more intimately

## Slide 4
The Gateway to VoIP World
System Application
Dinstar Technologies Co., Ltd.
Trust Growth Cooperation Sharing